## Slide 1: Travel Impacts of the COVID-19 Pandemic Preliminary Analysis
Kendall Mahavier, David Pace, and Don Pickrell
V0-321
July 29, 2020

## Slide 2: Two Views of the Post-Pandemic World
Carmageddon is coming!
  Most former transit riders and carpoolers will drive when they return to work
  As the economy reopens, traffic and congestion will overwhelm highways
Nobody will drive anywhere, and the Highway Trust Fund will go broke
  Most people will continue to work and shop at home
  Permanent reductions in driving and fuel use will starve the HTF
  But we won’t need any road construction, so who cares?
What should DOT be doing?

## Slide 3: What We Did
Used Vanderbilt University “Rebound Calculator” to estimate changes in commuting times in large urban areas as the economy recovers
Combined actual data and informed assumptions about factors affecting traffic levels and congestion
  Job losses and shifts to remote work
  Shifts from transit and carpool commuting to driving alone
Examined impacts in urban areas with high and low transit use
Developed scenarios for gradual resumption of travel activity
Estimated sustained remote work shares necessary to prevent gridlock

## Slide 4: Scenarios We Examined
Pre-pandemic baseline (Jan.-Feb. 2020)
Immediate aftermath (March-June 2020)
Improved testing, diagnosis, and treatment (mid-2021?)
Widespread vaccination (2022?)
Lingering or permanent impacts (beyond)

## Slide 5: Sample Urban Areas
Four population size categories
  Very large: >10 million (New York, Los Angeles)
  Large: 5-10 million (n=7)
  Medium: 3-5 million (n=7)
  Others: 1-3 million (n=6)
High and low transit use examples in each category
  Range is wide except in smallest size category
  Including carpooling (“private transit”) narrows the range

## Slide 6: Data Sources and Analysis Tools
Data sources
  2018 American Community Survey (Census Bureau): population, commuting mode shares, carpool composition, commute trip lengths
  IHS Global Insight: baseline employment, initial losses, and projected recovery
  Transit agency websites and press reports: ridership losses
  Univ. of Chicago study (April 2020): How Many Jobs Can be Done at Home?
Analysis tool: Vanderbilt Univ. “Rebound Calculator”
  Uses 2018 baseline data on employment, remote working, transit and carpool commuting
  Fits speed vs. travel volume relationships to historical data for sample cities
  Calculates impacts of job losses, remote work, and shifts from transit and carpooling to driving on average commuting times

## Slide 7: Baseline Data for Sample Cities (early 2020)
Population Category | Urban Area | pre-Pandemic Baseline Data |  |  |  |  | 
 |  | Population (thousands) (1) | Employment (thousands) (2) | Transit Commute Share (3) | Carpool Commute Share (3) | Remote Work Share (3) | Average Commute Time (minutes) (4)
> 10 million | New York | 19,216 | 10,019 | 30.9% | 6.3% | 4.7% | 31.0
 | Los Angeles | 13,215 | 6,288 | 4.8% | 9.5% | 5.9% | 31.6
5-10 million | Chicago | 9,459 | 4,771 | 12.1% | 8.0% | 5.4% | 30.1
 | Philadelphia | 6,102 | 2,995 | 9.8% | 7.2% | 5.5% | 28.7
 | Washington, D.C. | 6,280 | 3,380 | 13.0% | 9.2% | 6.1% | 34.3
 | Dallas | 7,573 | 3,851 | 1.3% | 9.5% | 5.8% | 28.8
 | Houston | 7,066 | 3,208 | 2.0% | 9.4% | 4.9% | 30.4
 | Miami | 6,166 | 2,732 | 3.1% | 9.2% | 5.7% | 29.9
 | Atlanta | 6,020 | 2,884 | 3.0% | 8.9% | 7.6% | 32.3
3-5 million | Boston | 4,873 | 2,814 | 13.2% | 7.0% | 5.5% | 31.7
 | San Francisco | 4,732 | 2,498 | 17.3% | 9.6% | 7.0% | 34.3
 | Seattle | 3,980 | 2,116 | 10.7% | 10.0% | 6.7% | 30.6
 | Minneapolis | 3,640 | 2,031 | 4.5% | 8.1% | 5.9% | 25.4
 | Phoenix | 4,948 | 2,220 | 1.8% | 11.2% | 7.4% | 26.1
 | Detroit | 4,320 | 2,048 | 1.3% | 8.6% | 4.3% | 27.4
 | San Diego | 3,338 | 1,516 | 2.6% | 8.8% | 6.6% | 26.9
1-3 million | Baltimore | 2,800 | 1,437 | 6.0% | 8.0% | 5.3% | 29.9
 | Portland | 2,942 | 1,230 | 6.1% | 8.8% | 8.1% | 27.0
 | Pittsburgh | 2,318 | 1,197 | 5.6% | 8.3% | 5.1% | 26.6
 | St. Louis | 2,803 | 1,398 | 2.1% | 6.9% | 4.6% | 25.9
 | Denver | 2,967 | 1,558 | 3.8% | 8.2% | 8.7% | 27.6
 | Charlotte | 2,637 | 1,251 | 1.5% | 9.4% | 7.3% | 27.4
Notes: Census Bureau, MSA population estimates 2019
IHS Global Insight, special tabulation provided to Volpe Center, 6/3/2020, data for 2019Q1
Tabulated from American Community Survey, 2018, Table S0802
Rebound Calculator https://lab-work.github.io/therebound/

## Slide 8: Immediate Impacts (March-June 2020)
Population Category | Urban Area | Estimated Changes from Baseline Values: March-June 2020 (percent) |  |  |  |  |  |  | 
 |  | Employment Loss (IHS forecast 2020 Q2) (5) | Decline in Transit Ridership (6) | Shift from Transit to SOV | Decline in Carpool Commuting (7) | Shift from Carpool to SOV | Maximum Remote Work Share (All Employment) (8) | Change in Remote Work Share from Baseline | Average Commute Time (minutes) (4)
> 10 million | New York | -19% | -90% | -72% | -56% | -45% | 42% | 37% | 26.7
 | Los Angeles | -20% | -80% | -76% | -56% | -45% | 39% | 33% | 24.1
5-10 million | Chicago | -18% | -88% | -81% | -56% | -44% | 39% | 34% | 26.1
 | Philadelphia | -19% | -97% | -90% | -56% | -43% | 40% | 35% | 21.8
 | Washington, D.C. | -17% | -85% | -77% | -56% | -45% | 50% | 44% | 32.8
 | Dallas | -18% | -75% | -72% | -56% | -42% | 40% | 34% | 25.3
 | Houston | -17% | -55% | -52% | -56% | -43% | 37% | 32% | 26.0
 | Miami | -21% | -80% | -77% | -56% | -46% | 37% | 31% | 24.0
 | Atlanta | -20% | -67% | -65% | -56% | -44% | 40% | 33% | 27.6
3-5 million | Boston | -20% | -92% | -84% | -56% | -43% | 44% | 39% | 24.0
 | San Francisco | -19% | -92% | -82% | -56% | -45% | 45% | 38% | 19.7
 | Seattle | -20% | -77% | -71% | -56% | -44% | 42% | 36% | 22.7
 | Minneapolis | -18% | -60% | -56% | -56% | -40% | 41% | 35% | 24.2
 | Phoenix | -20% | -45% | -41% | -56% | -41% | 39% | 32% | 24.4
 | Detroit | -22% | -80% | -77% | -56% | -42% | 35% | 31% | 24.8
 | San Diego | -18% | -65% | -63% | -56% | -44% | 40% | 33% | 21.7
1-3 million | Baltimore | -18% | -62% | -57% | -56% | -47% | 42% | 36% | 23.9
 | Portland | -19% | -70% | -66% | -56% | -42% | 39% | 31% | 21.7
 | Pittsburgh | -20% | -73% | -68% | -56% | -39% | 37% | 32% | 23.2
 | St. Louis | -19% | -40% | -38% | -56% | -41% | 38% | 33% | 20.6
 | Denver | -19% | -70% | -67% | -56% | -44% | 43% | 34% | 24.4
 | Charlotte | -20% | -52% | -51% | -56% | -40% | 38% | 31% | 24.4
Notes: (4) Rebound Calculator https://lab-work.github.io/therebound/
(5) Calculated from IHS Global Insight, special tabulation provided to Volpe Center, 6/3/2020
(6) U.S. Department of Transportation, Bureau of Transportation Statistics, Transportation Demand Early Indicators Report: Weekly Impact, 5/8/2020; And various news articles and transit agency websites
(7) Estimated from nationwide share of carpool commuters riding with members of same household, obtained from tabulation of American Community Survey PUMS conducted by Philip Winters, CUTR, University of South Florida; reported in e-mail message from Steve Polzin to Don Pickrell, 6/2/2020.
(8) assumed equal to maximum attainable remote work shares reported in Dingel & Neiman, "How Many Jobs Can be Done at Home?" https://bfi.uchicago.edu/wp-content/uploads/BFI_White-Paper_Dingel_Neiman_3.2020.pdf

## Slide 9: Improved Testing and Treatment (mid-2021?)
Population Category | Urban Area | Estimated Changes from Baseline Values: Early to Mid-2021 (percent) |  |  |  |  | 
 |  | Employment Loss (IHS forecast 2021Q2) | Shift from Transit to SOV | Shift from Carpool to SOV | Change in Remote Work from Baseline | Average Commute Time (minutes) | Change in Remote Work Share Necessary to Maintain Baseline Commute Time
> 10 million | New York | -14% | -44% | -24% | 19% | 25.7 | 8%
 | Los Angeles | -13% | -45% | -24% | 17% | 25.5 | 0%
5-10 million | Chicago | -12% | -49% | -23% | 17% | 26.9 | 0%
 | Philadelphia | -13% | -54% | -22% | 17% | 23.2 | 0%
 | Washington, D.C. | -11% | -46% | -25% | 22% | 32.9 | 0%
 | Dallas | -13% | -43% | -22% | 17% | 25.9 | 0%
 | Houston | -14% | -30% | -22% | 16% | 26.7 | 0%
 | Miami | -15% | -46% | -25% | 16% | 25.0 | 0%
 | Atlanta | -13% | -39% | -24% | 16% | 28.5 | 0%
3-5 million | Boston | -15% | -50% | -22% | 19% | 25.0 | 0%
 | San Francisco | -13% | -49% | -25% | 19% | 22.3 | 1%
 | Seattle | -14% | -42% | -24% | 18% | 24.0 | 0%
 | Minneapolis | -13% | -33% | -19% | 18% | 24.3 | 0%
 | Phoenix | -14% | -24% | -21% | 16% | 24.7 | 0%
 | Detroit | -16% | -45% | -22% | 15% | 25.2 | 0%
 | San Diego | -12% | -37% | -24% | 16% | 22.7 | 0%
1-3 million | Baltimore | -12% | -34% | -27% | 18% | 24.9 | 0%
 | Portland | -13% | -40% | -22% | 15% | 22.9 | 0%
 | Pittsburgh | -14% | -40% | -18% | 16% | 23.8 | 0%
 | St. Louis | -13% | -22% | -20% | 16% | 21.6 | 0%
 | Denver | -14% | -40% | -24% | 17% | 24.9 | 0%
 | Charlotte | -12% | -31% | -20% | 15% | 25.1 | 0%
Assumption | Value
Fraction of Former Transit Riders Returning | 40%
Fraction of Non-Household Carpool Members Returning | 40%
Fraction of Maximum Remote Work Share Continuing to Work Remotely | 50%

## Slide 10: Widespread Vaccination (2022?)
Population Category | Urban Area | Estimated Changes from Baseline Values: 2022 (percent) |  |  |  |  | 
 |  | Employment Loss (IHS forecast 2022Q2) | Shift from Transit to SOV | Shift from Carpool to SOV | Change in Remote Work from Baseline | Average Commute Time (minutes) | Change in Remote Work Share Necessary to Maintain Baseline Commute Time
> 10 million | New York | -8% | -21% | -9% | 9% | 29.3 | 4%
 | Los Angeles | -8% | -22% | -9% | 8% | 27.6 | 0%
5-10 million | Chicago | -7% | -24% | -7% | 8% | 28.2 | 0%
 | Philadelphia | -7% | -26% | -7% | 9% | 25.2 | 0%
 | Washington, D.C. | -5% | -23% | -10% | 11% | 33.5 | 0%
 | Dallas | -6% | -20% | -6% | 8% | 27.1 | 0%
 | Houston | -8% | -14% | -7% | 8% | 27.9 | 0%
 | Miami | -7% | -23% | -10% | 8% | 26.9 | 0%
 | Atlanta | -5% | -19% | -9% | 8% | 30.2 | 0%
3-5 million | Boston | -8% | -25% | -7% | 10% | 27.5 | 0%
 | San Francisco | -7% | -24% | -10% | 9% | 27.8 | 1%
 | Seattle | -8% | -21% | -9% | 9% | 26.4 | 0%
 | Minneapolis | -6% | -16% | -4% | 9% | 24.8 | 0%
 | Phoenix | -6% | -11% | -6% | 8% | 25.3 | 0%
 | Detroit | -9% | -21% | -6% | 8% | 25.9 | 0%
 | San Diego | -6% | -18% | -8% | 8% | 24.3 | 0%
1-3 million | Baltimore | -6% | -16% | -11% | 9% | 26.8 | 0%
 | Portland | -6% | -20% | -6% | 8% | 24.5 | 0%
 | Pittsburgh | -8% | -19% | -2% | 8% | 24.8 | 0%
 | St. Louis | -8% | -10% | -4% | 8% | 23.0 | 0%
 | Denver | -6% | -20% | -8% | 8% | 26.1 | 0%
 | Charlotte | -4% | -15% | -4% | 8% | 26.1 | 0%
Assumption | Value
Fraction of Former Transit Riders Returning | 70%
Fraction of Non-Household Carpool Members Returning | 70%
Fraction of Maximum Remote Work Share Continuing to Work Remotely | 25%

## Slide 11: Residual Impacts (beyond 2022)
Population Category | Urban Area | Estimated Changes from Baseline Values: Post-2022 |  |  |  |  | 
 |  | Employment Loss (IHS forecast 2023Q4) | Shift from Transit to SOV | Shift from Carpool to SOV | Change in Remote Work from Baseline | Average Commute Time (minutes) | Change in Remote Work Share Necessary to Maintain Baseline Commute Time
> 10 million | New York | -3% | -14% | -3% | 7% | 30.3 | 5%
 | Los Angeles | -3% | -14% | -4% | 7% | 28.9 | 0%
5-10 million | Chicago | -2% | -16% | -2% | 7% | 28.9 | 1%
 | Philadelphia | -1% | -17% | -2% | 7% | 27.0 | 2%
 | Washington, D.C. | 1% | -15% | -5% | 9% | 33.9 | 5%
 | Dallas | 1% | -13% | -1% | 7% | 27.9 | 2%
 | Houston | -1% | -9% | -2% | 6% | 29.2 | 0%
 | Miami | 2% | -15% | -5% | 6% | 29.1 | 3%
 | Atlanta | 4% | -13% | -3% | 7% | 31.9 | 5%
3-5 million | Boston | -1% | -17% | -2% | 8% | 29.7 | 3%
 | San Francisco | 0% | -16% | -5% | 8% | 31.7 | 5%
 | Seattle | -1% | -14% | -4% | 7% | 28.6 | 2%
 | Minneapolis | 0% | -10% | 1% | 7% | 25.1 | 2%
 | Phoenix | 3% | -6% | -1% | 6% | 25.9 | 4%
 | Detroit | -3% | -13% | -1% | 6% | 26.5 | 0%
 | San Diego | 0% | -12% | -3% | 7% | 25.5 | 1%
1-3 million | Baltimore | 0% | -10% | -6% | 7% | 28.4 | 2%
 | Portland | 0% | -13% | -1% | 6% | 25.9 | 2%
 | Pittsburgh | -3% | -12% | 3% | 6% | 25.5 | 0%
 | St. Louis | -2% | -7% | 1% | 7% | 24.1 | 0%
 | Denver | 1% | -13% | -3% | 7% | 26.9 | 2%
 | Charlotte | 4% | -10% | 1% | 6% | 27.2 | 5%
Assumption | Value
Fraction of Former Transit Riders Returning | 80%
Fraction of Non-Household Carpool Members Returning | 80%
Fraction of Maximum Remote Work Share Continuing to Work Remotely | 20%

## Slide 12: Potential Evolution of Impacts: New York
Chart: Commute Time (Minutes)
| Baseline | Immediate Impacts | Improved Testing and Treatment | Widespread Vaccination | Residual Impacts
Travel Time | 31 | 24.1 | 25.7 | 29.3 | 30.3
Increase in Remote Work from Baseline | 0 | 0.37 | 0.19 | 0.09 | 0.07
Shift from Transit Use to SOV from Baseline | 0 | 0.72 | 0.44 | 0.21 | 0.14

## Slide 13: Conclusions
Most cities saw large reductions in commuting times during the immediate aftermath of the pandemic
With 80% return to transit and carpooling, and employment back to pre-pandemic levels, only modest (3-4%) increases in remote working would be necessary to prevent increased commuting times
  New York and San Francisco would need ~6% increases
  But pre-pandemic remote work shares were only 4-8%, so adding 3-4% is a lot
Intuition: almost everyone was already driving, except in a few cities

## Slide 14: Limitations of Our Analysis
Significant uncertainties about the pandemic and recovery remain:
  Timing of recovery phases (more reliable testing, improved treatment, widespread vaccination)
  Extent and timing of restoration in transit capacity
Modeling limitations:
  Commuting times and estimated changes are averages over entire urban areas, and both will vary widely within individual urban areas
    Highway capacity and transit service vary widely across commuting corridors within urban areas
    Geographic distribution of workplaces and preferred departure times also affect commuting times
  Relationships between travel volume and speed apply to entire urban areas, including all modes and travel hours, and are only approximate

## Slide 15: Critical Uncertainties
How much of transit capacity will ultimately be restored, and when?
  Depends partly on cleaning protocols, passenger management practices
  But also depends on traveler reactions, car ownership among former transit users, where commuters’ jobs are located
How widespread will remote working remain?
  What industries and occupations lend themselves to it?
  How much of total employment do they account for?
  Will industries where it can work continue to embrace it?
  How many employees have suitable spaces, and want to use them?

## Slide 16: What Can DOT Do to Address Congestion?
Focus on solutions to congestion, treating modes as an interdependent system
  Work with transit agencies to develop most effective methods to restore service, capacity, and rider confidence
  Identify industries and occupations amenable to sustained remote working and encourage it through existing programs
    Seemingly amenable: government, technology, finance, education
    Probably not: health care, manufacturing, retail, food service
Identify and promote helpful changes in travel behavior
Search for policy and technology responses to mitigate changes that increase congestion

## Slide 17: Potential Follow-On Analysis: Updates
Update the analysis as new information becomes available
  What if transit capacity takes longer to restore, or never gets back to 100%?
  What if non-household carpool members never re-join?
  What will it take to sustain increases in remote working?
    Remote work shares have only increased by 3-4 percentage points over the past decade, even with huge improvements in remote network access and sharing platforms
    How many employers (and employees) actually want to continue it?
Explore how to incorporate geographic and time-of-day variation into the model, to enable identification of specific problem areas and additional solutions